## Slide 1
BAREJA TERMINAL OPERATION
Presented By,
Sanjiv Ranjan
Samir Kumar Nayak
Sadiq Syed
Tuneer Bhattacherjee
Sahil Hansraj Nagrale
Sagar Singh Rathore
Anurag Gupta
Supandeep Grewal
Saurabh Dubey

## Slide 2
Overview
Receipt
Storage
Quality
Dispatch
DISPATCH
STORAGE
QUALITY
OPERATIONS IN BAREJA TERMINAL
RECEIPT

## Slide 3
Reciept
1.KSPL
Multi-product pipeline
Ahmedabad ToP
2.KAPL
Dedeicated pipeline for ATF
Supplies to whole Gujraat, touches few places in Rajsthan.
Overview
Receipt
Storage
Quality
Dispatch

## Slide 4
INTERFACE CUTTING
MS
SKO
HSD
MS
PCK
PCK
PCK
2% OF MS
+
2% OF HSD
2% OF SKO
+
2% OF MS
2% OF HSD
+
2% OF SKO
Done by pipeline division at exchange pit
Overview
Receipt
Storage
Quality
Dispatch

## Slide 5
2A
3B
2B
3A
4D
4C
4A
4B
SKO/ATF
HSD
1C
1B
1A
MS
6A
6B
ETHANOL
UG & HZ
5A
5B
5C
WATER
TANKS
Overview
Receipt
Quality
Storage
Dispatch
Storage Tank Farm

## Slide 6
Tank Capacities & Storing Limit
Storage Tank | Quantity | Level Filled | Tank Dia.
MS | 3 | 8300KL | 24M
HSD | 4 | 11000KL | 32M
ATF | 2 | 6300KL | 28M
SKO | 2 | 3300KL | 18M
ETHANOL | 2 | 70KL | 
WATER | 3 | 2600KL/ 5200KL | 
Overview
Receipt
Quality
Storage
Dispatch
Types of tanks
Tanks are classified in the three ways:
Under ground and above ground tanks.
Floating roof and cone roof tanks.
Horizontal and vertical tanks.
For MS floating roof tanks are used to prevent evaporation.
Floating roof locks down at 1.25 meter.

## Slide 7
Mode of Tanks
Receipt
Closed
Opened
Dispatch
Opened
Closed
Dormant
Closed
Closed
Product is being received either from Pipeline or other Tanks.
No Dispatch occurs during this period.
Tank is Ideal. No dispatch or receiving is done.
Due to maintenance or other reasons.
Product is dispatched to TLF or other Tanks.
No receiving Operation occurs during this period.
Overview
Receipt
Quality
Storage
Dispatch

## Slide 8
Tank Level Alarms while storing
H
  Tank level Warning.
HH
  Tank level crossed permissible limit.
  Receipt Valve is Closed.
HHH
  Critical Height reached.
  Emergency Shutdown occurs.
While Receiving Product
While Dispatching Product
L
  Tank level Warning.
LL
  Dispatch Valve is Closed.
  Tank Level below permissible limit.
LLL
  Critical level reached.
  Emergency Shutdown occurs.
Overview
Receipt
Quality
Storage
Dispatch

## Slide 9
Storage Tank Pipe Valves
TANK
DBBV
ROSOV
Primary Valve Inlet
ROSOV
DBBV
Primary Valve Outlet
Secondary Valve Outlet
Overview
Receipt
Quality
Storage
Dispatch

## Slide 10
Overview
Receipt
Quality
Storage
Dispatch
Quality and Quantity at Different Stages
Refinery
Pipeline
Marketing Acknowledgement
Batch Formation Test
TLF Quality Checks
Consumer End Checks
Receive the test reports
Quantity
Valve Checks
Inform Terminal about the receipt
Guaging of tanks
Valve checks
Acknowledgement to pipeline
Settling in storage
Sampling
Tests report generated
Density Test
Surprise Test
Sample for MDG
Density Test
Water Test
Sedimentary Test

## Slide 11
Overview
Receipt
Quality
Storage
Dispatch
Batch Formation Test
TLF Checks
Settling time of one hour
Sample from Top, Bottom and Middle
9 different tests are performed
Density, Distillation, Sulphur, Copper, ROE, Appearance, Color, RON
Tests are carried Monthly, weekly and MDG
Test reports are issued to Control Room
MS, HSD, SKO
ATF
Settling time of two hours
Sample from Upper, Lower and Middle
21 different tests are performed
Tests are carried Monthly, weekly and MDG
Test reports are issued to Control Room
Every TT carries the test report
Density Checks
Water Checks
Sedimentary Checks
Dip Checks
MS should be in the first compartment
SKO & HSD –> Minimum 35 Degree Celsius
ATF –> Minimum 38 Degree Celsius
HSD –> 815 – 845 kg/m3
ATF –> 775 - 840 kg/m3
MS –>720 – 775 kg/m3
Standard Measure
Density
Flash Points

## Slide 12
Overview
Receipt
Storage
Quality
Dispatch
Type of Customers
Retail Outlets
Consumers - Bulk
Dispatch is done through Tank Trucks
Dealer Owned
Consortium
Transporter
Consumer Sales
Priority Dealers
COCO
Non Priority Dealers
Priority of the Customer
Demand Sensing
Through SMS
Through Xsparsh Web Application
Tankers are epicoated to prevent any chemical reaction
ATF has dedicated TT’s

## Slide 13
Overview
Receipt
Storage
Quality
Dispatch
Dispatch of TT

## Slide 14
Overview
Receipt
Storage
Quality
Dispatch
TLF Flow